## Slide 1: Iot
Reading / Writing analogue devices LED + Game-controller

## Slide 2: Recapitulation
Start up the Raspberry Pi
  Burn the image to SD-card
  See / get access to the R-Pi – some problems to make the windows update DNS
    https://github.com/adafruit/Adafruit-Pi-Finder
  Try the Linux environment
Start of the Python programming
  Simple GPIO access
  Remember to use Pyhon3

## Slide 3: LED light (RGB)

## Slide 4: LED controls
Set RGB to on|off (True | False )
GPIO.setmode(GPIO.BCM)
GPIO.setup(14, GPIO.OUT)
GPIO.setup(15, GPIO.OUT)
GPIO.setup(18, GPIO.OUT)
GPIO.output(14, GPIO.LOW)
GPIO.output(15, GPIO.HIGH)
GPIO.output(18, GPIO.HIGH)
Set RGB to different level
  PWM Pulse-Width Modulation
  Could also be useful when working with motors

## Slide 5: Pulse-Width Modulation
“Do you remember when you were a kid, how you sometimes flicked the light switch on and off repeatedly, really quickly, to see what would happen?
And you were told not to do it in case something bad happened (and it never did)? That was crude PWM.”
raspi.tv

## Slide 6: Pulse-Width Modulation
Frequency
Duty Cycle

## Slide 7: PWM Python example
GPIO.setup(25, GPIO.OUT) ← set the pin to be output
p = GPIO.PWM(25, 50) ← activate PWM at 50 hertz (frequency)
p.start(50) ← start PWM with a 50% Duty Cycle
p.ChangeFrequency(100) ← Change frequency
p.ChangeDutyCycle(20) ← Set the Duty Cycle to 20%
p.stop()

## Slide 8: Recapitulation
Start up the Raspberry Pi
  Burn the image to SD-card
  See / get access to the R-Pi – some problems to make the windows update DNS
    https://github.com/adafruit/Adafruit-Pi-Finder
  Try the Linux environment
Start of the Python programming
  Simple CPIO access
  Remember to use Pyhon3

## Slide 9: NOW
Your turn to work